Review Question 2

due to 6/3

- Assume a data stream is made of ten 0s. Encode this stream using the following encoding schemes. How many changes (vertical line) can you find for each scheme?

  - unipolar

  - polar NRZ-L

  - polar NRZ-I

  - RZ

  - Manchester

  - differential Manchester

- We measure the performance of a telephone line (4 kHz of bandwidth). When the signal is 10 V, the noise is 5 mV. What is the maximum data rate supported by this telephone line?

- Given a 10-bit sequence 1010011110 and a divisor of 1011, find the CRC. Check your answer.

- Draw the sender and receiver windows for a system using go-back-n ARQ given the following:

  - Frame 0 is sent; frame 0 is acknowledged.

  - Frames 1 and 2 are sent; frame 1 and 2 are acknowledged.

  - Frames 3, 4, and 5 are sent; NAK 4 is received.

  - Frame 4, 5, 6, and 7 are sent; frames 4 through 7 are acknowledged.

5. Repeat Question 4 using selective-reject ARQ.